## Slide 1: RoboRacer Autonomous Racing
HANDS-ON WORKSHOP
Write a Python driving algorithm and race it in the AutoDRIVE simulator
Windows · macOS · Docker · Python
Notes: Welcome everyone. Today you'll write the brain of a small autonomous race car: a single Python function that reads LiDAR and decides speed and steering. Everything runs in a simulator on your laptop, so crashes are free.

## Slide 2: Today's race plan
01
Meet RoboRacer
History, the car, how races work and how the software thinks
02
Setup
Start the simulator and the Docker containers
03
The drive() API
One Python function: sensors in, commands out
04
Algorithms
Emergency braking, wall following, Follow the Gap, Pure Pursuit
05
Exercises
Build, tune and race your controller
Notes: Five parts. We start with the ideas, get everyone's simulator running, learn the one function you write, look at the classic RoboRacer algorithms, and then spend most of the time building and racing.

## Slide 3: Meet RoboRacer
01
Where it came from, what the car is made of, how races work and how the software thinks

## Slide 4: What is RoboRacer?
1/10-scale autonomous racing
RoboRacer (formerly F1TENTH) is a global community that races small self-driving cars.
Onboard sensors only
Cars see the track with a 2D LiDAR and know their speed and pose from odometry.
Real autonomy skills
Perception, planning and control: the same pipeline as full-size self-driving cars.
Simulator first
Today we use the AutoDRIVE simulator from the official ICRA 2026 sim-racing release.
1/10
vehicle scale
0.324 m
wheelbase used for steering maths
20 Hz
how often your code is called
Notes: RoboRacer, previously known as F1TENTH, is an international autonomous racing community using one-tenth scale cars. The cars only use onboard sensors, mainly a 2D LiDAR plus odometry. The skills are the same ones used in full-size autonomous vehicles. Today we use the official AutoDRIVE simulator so nobody needs hardware.

## Slide 5: Why race robots?
Racing is autonomy at the limit
A race has one clear goal and an unforgiving referee: the stopwatch. Every shortcut in your software shows up as a slower lap or a crash.
Goal: the fastest lap without a collision
Speed exposes weaknesses
At the limit, every delay, noisy reading or bad estimate becomes visible.
Cheap to fail
A 1/10-scale car, or a simulator, turns expensive mistakes into quick lessons.
Skills transfer
Perception, planning and control are the same problems full-size self-driving cars solve.
Notes: Why racing? Because it gives autonomy a clear, measurable objective. On a normal road you can drive slowly and hide weaknesses. On a race track, latency, sensor noise and poor planning cost you time or end in a crash. Small cars and simulators make those failures cheap, and the skills carry straight over to full-size autonomous vehicles.

## Slide 6: From F1TENTH to RoboRacer
2016
Founded at Penn
Started at the University of Pennsylvania under the name F1TENTH.
Growing
A global community
Teaching modules used at 80+ universities; races at major robotics conferences.
2024
Sim Racing League
Virtual races on an AutoDRIVE digital twin debut at IROS 2024 and CDC 2024.
2025
Sim racing grows
The ICRA 2025 sim race drew 58 teams and more than 150 participants.
2026
ICRA 2026, Vienna
Physical race with time trials and head-to-heads. Our simulator comes from the 2026 release.
Notes: RoboRacer began in 2016 at the University of Pennsylvania as F1TENTH, a play on Formula 1 at one-tenth scale. It grew into an international community: universities teach its course and teams race at big robotics conferences such as ICRA and IROS. Since 2024 there has also been a simulated league on the AutoDRIVE digital twin, which is the same simulator we use today, from its ICRA 2026 release.

## Slide 7: Build · Learn · Race
Build
An open-source 1/10-scale race car: parts list, build guide and a ROS 2 driver stack.
Today: We drive its digital twin in AutoDRIVE
Learn
A university course on perception, planning and control, in 4-, 10- and 15-week versions.
Today: A taste: reactive driving and Pure Pursuit
Race
Competitions at international robotics conferences, both physical and simulated.
Today: Race your own controller around the sim track
Notes: RoboRacer rests on three pillars. Build: the car design is open source, so anyone can build one. Learn: there is a full course on the foundations of autonomy that universities can adopt. Race: competitions give everyone a shared, measurable goal. Today touches all three, in miniature.

## Slide 8: Inside a RoboRacer car
1
2
3
4
5
6
1
2D LiDAR
Hokuyo UTM-30LX or 10LX: a 270° laser scan, about 40 times a second.
2
Onboard computer
NVIDIA Jetson (Xavier NX in the official build) running ROS 2.
3
VESC motor controller
Drives the motor and reports wheel speed for odometry.
4
Steering servo
Turns the front wheels to the commanded angle.
5
LiPo battery
Powers the motor, computer and sensors.
6
Chassis
Traxxas Slash 4x4: a 1/10-scale RC truck as the base.
Simplified side view, car facing right. Exact parts vary by build.
Notes: This is what's inside the real car. On top: the LiDAR, which is the main sensor, and a Jetson computer running ROS 2. Underneath: the VESC electronic speed controller, which also measures wheel speed for odometry, the steering servo and the battery, all on a Traxxas RC chassis. The simulator models the same sensors and actuators, so code written today follows the same pattern as code for the real car.

## Slide 9: How the races work
Physical races
e.g. ICRA 2026
1
Time trial
Solo laps against the clock on the real track.
2
Head-to-head
Two cars on track at once: overtake safely to advance.
Sim Racing League
AutoDRIVE digital twin
1
Qualification
Complete multiple laps on a practice track without hitting the bounds.
2
Time attack
Race the clock on a previously unseen track.
Sim teams submit their code as a Docker container, the same way this workshop runs yours.
Notes: Physical races, like the one at ICRA 2026 in Vienna, usually start with a time trial: one car, fastest laps. Then cars race head to head, which adds overtaking and opponent awareness. The simulated league starts with qualification, proving you can lap reliably without touching the walls, then a time attack on a track nobody has seen before, so you can't hard-code the circuit. The motto is simple: drive fast, but don't crash.

## Slide 10: How an autonomous car thinks
SENSE
What is around me?
LiDAR: distance to walls all around the car
Odometry: speed, position and heading
PLAN
Where should I go?
Your drive() function
Find free space, pick a direction and a speed
ACT
Make it happen
Speed (m/s) becomes throttle
Steering angle turns the front wheels
Repeats about 20 times per second, so every call must return quickly
Notes: Every autonomous system follows sense, plan, act. The workshop runtime handles sense and act for you. Your job is the middle box: given the latest sensor snapshot, decide one speed and one steering angle. Then it happens again about 50 ms later.

## Slide 11: The autonomy stack
Sense
LiDAR scan, wheel odometry, IMU
RUNTIME
Perceive
Clean the scan; find walls, gaps and opponents
TODAY
Localize
Build a map (SLAM) and track where the car is on it
NEXT STEP
Plan
Choose a path: a gap, a wall offset or a raceline
TODAY
Control
Turn the path into steering and speed
TODAY
Act
Motor controller and steering servo
RUNTIME
Today you build the red stages without a map: that is reactive driving. Map-based racing adds localization and an optimised raceline.
Notes: Sense-plan-act expands into a pipeline. Sensors and actuators are handled by the workshop runtime. Today you write a simple perception, planning and control layer that only looks at the current scan. The fast teams also build a map of the track with SLAM, localize on it with a particle filter, and follow a precomputed raceline with Pure Pursuit or model predictive control. That's the natural next step after this workshop.

## Slide 12: Two ways to drive a race
Reactive
TODAY
HOW IT WORKS
React to the latest LiDAR scan only. No map.
ALGORITHMS
Wall following, Follow the Gap, emergency braking
STRENGTH
Simple, and works on any track immediately
WATCH OUT
Short-sighted: it can't plan a fast line through corners
Map-based
NEXT STEP
HOW IT WORKS
Map the track first, then localize on it every scan.
ALGORITHMS
SLAM, particle filter, raceline optimisation, Pure Pursuit or MPC
STRENGTH
Fastest laps: it plans the whole lap in advance
WATCH OUT
More parts to tune; a localization error can cause a crash
Notes: There are two broad families of racing software. Reactive methods look only at the current scan, so they're simple and work on a brand-new track, but they can't plan ahead. Map-based methods first drive slowly to build a map, then plan an optimal raceline and track it at speed. Most winning teams use map-based stacks with a reactive fallback for safety. Today we stay reactive.

## Slide 13: Simulate first, then go real
Safe
Crashes cost nothing: reset the car and try again.
Fast
Edit, restart and test a change in seconds.
Reproducible
Same track, same car, same conditions for everyone.
The sim-to-real gap: what changes on a real car
Sensor noise
Reflections, glass and black surfaces give odd LiDAR readings.
Tyre grip
Tyres slip, so the car doesn't turn exactly as commanded.
Latency
Real compute and messages add delay between sensing and acting.
Battery
Voltage drops as it drains, so the same throttle gives less speed.
Notes: Teams develop in simulation because it's safe, quick and fair. But a simulator is never perfect. Real LiDARs see strange returns from shiny or dark surfaces, real tyres slip, real computers add latency and real batteries sag. Robust code that slows down when unsure and doesn't trust a single ray is far more likely to survive the jump to a real car.

## Slide 14: Words you'll hear today
LiDAR
A laser scanner that measures the distance to surfaces around the car, ray by ray.
Odometry
An estimate of speed and position from wheel motion, often fused with an IMU.
ROS 2
Robot Operating System: middleware that passes sensor and command messages between programs.
Docker
Packages software into containers so it runs the same on every computer.
SLAM
Simultaneous Localization And Mapping: build a map while tracking your position in it.
Raceline
The fastest path around the track, usually planned in advance from a map.
Lookahead
How far ahead the controller aims. Longer is smoother; shorter is more precise.
Digital twin
A simulated copy of the real car and track, with matching sensors and dynamics.
Notes: A quick vocabulary check before we set up. You don't need to know ROS 2 or Docker to take part today; the launcher hides them. But you'll see these words in the logs and in RoboRacer material, so it helps to know what they mean.

## Slide 15: Setup
02
Start the simulator, connect the car and learn the launcher commands

## Slide 16: How the pieces connect
AutoDRIVE Simulator
Unity app on your computer
ROS bridge
Docker container
Controller runtime
Docker container
controller.py
your drive() function
Socket.IO
port 4567
LiDAR, odom
throttle, steer
Observation
DriveCommand
Everything runs in Docker
No ROS, AVLite or Python install needed on your laptop.
Live code reload
Source files are mounted live: save, then restart. No image rebuild.
One bridge per port
Only one simulator bridge can own port 4567. Stop other projects first.
Notes: The simulator runs natively on your machine. A ROS bridge container talks to it over Socket.IO on port 4567. The controller runtime container turns ROS messages into a simple Observation, calls your drive() function, and sends the resulting command back. Your code is mounted into the container, so editing and restarting is fast.

## Slide 17: Start the workshop
1
Install Docker Desktop
Linux containers. The first start needs Internet to download the simulator and API image.
2
Open a terminal in this folder
PowerShell on Windows, Terminal on macOS.
3
Run the start command
Downloads on first run, then launches the simulator and containers.
4
Choose Connection + Autonomous
In the simulator connect to 127.0.0.1:4567 and switch to Autonomous mode.
WINDOWS · POWERSHELL
.\workshop.ps1 start
# If Windows blocks the script:
Set-ExecutionPolicy -Scope Process -ExecutionPolicy Bypass
MACOS · TERMINAL
./workshop.sh start
# Apple silicon: enable Rosetta in Docker Desktop
# App blocked? Right-click it, choose Open
Notes: Ideally computers were prepared before the session because the first start downloads the simulator and Docker image. On Apple silicon, Docker Desktop needs 'Use Rosetta for x86_64/amd64 emulation' because the API image is amd64 only. Once the simulator opens, click Connection, confirm 127.0.0.1:4567, then choose Autonomous. The starter controller deliberately keeps the car stopped.

## Slide 18: Launcher cheat sheet
Goal | Windows | macOS | What it does
Start | .\workshop.ps1 start | ./workshop.sh start | Launch sim + containers
Reload code | .\workshop.ps1 restart -Controller starter | ./workshop.sh restart -c starter | Reload your saved code
Try example | .\workshop.ps1 restart -Controller example | ./workshop.sh restart -c example | Run Follow the Gap demo
Pause | .\workshop.ps1 pause | ./workshop.sh pause | Stop driving, keep sim open
Logs | .\workshop.ps1 logs -Follow | ./workshop.sh logs -f | See errors and messages
Status | .\workshop.ps1 status | ./workshop.sh status | Show container state
Test | .\workshop.ps1 test | ./workshop.sh test | Python checks, no driving
Stop | .\workshop.ps1 stop | ./workshop.sh stop | Close sim, keep downloads
Before switching controllers: pause, then reset the car in the simulator.
Notes: These are the only commands you need. Restart reloads your saved Python. The selected controller is remembered, so use '-Controller starter' (or '-c starter' on macOS) to get back to your own code after trying the example. Logs with follow is your best friend when something goes wrong.

## Slide 19: The drive() API
03
One function: a sensor snapshot comes in, a driving command goes out

## Slide 20: The one function you write
CONTROLLER.PY
from workshop_api import DriveCommand, Observation
def drive(observation: Observation) -> DriveCommand:
# 1. Look at observation.ranges / .sector()
# 2. Choose a steering angle from free space
# 3. Choose a speed (slower in corners)
# 4. Return one command, no loops or sleep
return DriveCommand(speed_mps=0.0,
steering_rad=0.0)
IN: Observation
A sensor snapshot: LiDAR ranges, measured speed, pose and dt.
OUT: DriveCommand
speed_mps (up to 1 m/s) and steering_rad (±30°, positive = left).
Starts stopped
The starter returns DriveCommand(), so the car waits until you edit it.
Notes: This is the entire interface. The runtime calls drive() about 20 times per second with the newest Observation. You return a DriveCommand. All distances are metres and all angles radians. The starter returns the default command, which is zero speed and zero steering.

## Slide 21: Reading the LiDAR scan
0 rad (ahead)
+π/2
left
−π/2
right
angle_i = angle_min + i * angle_increment
ranges[i] is a distance in metres
One reading per ray, swept around the car.
0 means unknown
Not evidence of a clear road: treat it as blocked.
range_max means clear
Nothing hit within the sensor limit (hollow dots).
Angles are radians
0 is straight ahead, positive is left, negative is right.
Forward cone: observation.sector(-0.2, 0.2)
Notes: The LiDAR fires rays all around the car and reports the distance each ray travels. Ray i points at angle_min plus i times angle_increment. Zero means the reading was invalid or unknown, so never treat it as free space. A reading equal to range_max means the ray saw nothing, i.e. clear. The sector() helper returns all ranges between two angles; sector(-0.2, 0.2) is roughly the 23-degree cone straight ahead, shown in red.

## Slide 22: Observation and command reference
observation. | Meaning | Units
ranges | LiDAR distances; 0 = unknown, range_max = clear | m
angle_min angle_increment | Angle of ray i = angle_min + i × angle_increment | rad
sector(low, high) | Ranges between two angles in [−π, π] | m
speed_mps | Measured forward speed (not throttle) | m/s
x, y, yaw | Car position and heading in the simulator world | m, rad
dt | Time since the previous control tick | s
DriveCommand(...)
speed_mps
Requested forward speed. Capped at 1 m/s.
steering_rad
Front wheel angle. Capped at ±30°, positive turns left.
DriveCommand() = stop
Notes: Quick reference to keep open while coding. Note that speed_mps in the observation is the measured speed, while speed_mps in the command is the speed you request; the runtime converts it into simulator throttle. Pose is in simulator world coordinates, handy later for lap analysis.

## Slide 23: Rules of the loop and safety nets
Your rules
Return within 0.1 s
Slower calls stop the controller.
No loops or sleep
Return one command per call; the runtime runs the loop.
Unsure? Stop.
Return DriveCommand() when no valid choice exists.
Errors stop the car
Exceptions or invalid output halt it until you fix and restart.
Runtime safety nets
Hard limits
Speed capped at 1 m/s, steering at ±30°.
Command expiry
The bridge drops commands older than 0.5 s, even if your code hangs.
Front guard
Throttle is cut if anything is within 0.35 m in the ±12° front cone.
Not a crash shield
Zero throttle is not an instant stop. Brake early yourself.
Notes: On the left are the rules your code must follow; breaking them stops the controller and the logs tell you why. On the right are the protections the runtime adds. They exist so a bug can't send the car off at full speed, but they are not full collision avoidance: your algorithm still has to drive safely.

## Slide 24: Driving algorithms
04
The classic RoboRacer toolkit: brake, follow a wall, follow the gap, steer smoothly

## Slide 25: Safety first: time to collision
TTC = r / max(v·cos θ, 0)
Seconds until we reach what this ray sees
r
Range of the ray, in metres
v · cos θ
How fast we close in along that ray
Brake
If a front ray reads 0 or its TTC drops below a limit (e.g. 0.8 s)
AUTOMATIC EMERGENCY BRAKING
import math
from workshop_api import DriveCommand, wrap_angle
def too_close(obs, ttc_limit=0.8):
for i, r in enumerate(obs.ranges):
a = wrap_angle(obs.angle_min + i * obs.angle_increment)
if abs(a) > math.radians(45):
continue # only look ahead
closing = obs.speed_mps * math.cos(a)
if r == 0 or (closing > 0 and r / closing < ttc_limit):
return True # unknown or about to hit
return False
# in drive(): if too_close(observation): return DriveCommand()
Notes: Before making the car fast, make it safe. Time to collision divides the distance along a ray by how quickly we approach along that ray. If any forward ray predicts a collision soon, or is unknown, return a stop command. At low speed TTC alone lets the car creep into a wall, so combine it with a minimum distance check, which is exercise 2.

## Slide 26: Wall following
wall
b
a
θ
D
L
1
Measure two rays
b at +90° (left); a at θ ≈ 40° further forward
2
Wall angle and distance
α = atan((a·cos θ − b) / (a·sin θ)); D = b·cos α
3
Look ahead
D′ = D + L·sin α (where the car will be)
4
PD steering
e = d_target − D′; steering = −(Kp·e + Kd·ė)
Left wall shown. For the right wall use −90° rays and flip the steering sign.
Notes: Wall following keeps a fixed distance from one wall. Two rays to the same wall let you compute the car's angle to the wall, alpha, and its current distance D. Because the car moves while you react, predict the distance a lookahead L ahead. The error between your target distance and that prediction drives a PD controller. Positive error means too close to the left wall, so steer right, hence the minus sign. Start with Kd = 0 and tune Kp until it tracks without oscillating.

## Slide 27: Follow the Gap
1
Look ahead
Keep rays within ±80° and cap ranges at 3 m
2
Inflate obstacles
Block rays under 1.2 m plus a 0.25 m safety bubble
3
Find the widest gap
Group neighbouring free rays; keep the largest
4
Aim at its middle
Steer toward the gap centre with Pure Pursuit
aim here
+80° (left)
0° (ahead)
−80° (right)
blocked
safety bubble
free
chosen gap
Notes: This is what examples/follow_the_gap.py does. Each bar is one LiDAR ray, its height the measured range. Close readings are blocked, and a bubble about the car's half-width is added around them so we don't clip corners. The longest run of free rays is the best gap, and we aim at its middle. The example uses exactly these numbers: plus or minus 80 degrees, 3 m cap, 1.2 m threshold, 0.25 m bubble. It's a teaching example, not a verified clean-lap solution, so try to improve it.

## Slide 28: Pure Pursuit steering and speed
δ = arctan( 2b · sin α / L )
b = 0.324 m wheelbase · α = bearing to target · L = lookahead
heading
L
α
target (e.g. gap centre)
predicted arc
Chart: speed = 0.8 / (1 + 2|δ|)
| 0° | 5° | 10° | 15° | 20° | 25° | 30°
Requested speed (m/s) | 0.8 | 0.68 | 0.59 | 0.53 | 0.47 | 0.43 | 0.39
Slow down as steering grows: corners need less speed.
Notes: Pure Pursuit turns 'I want to go there' into a wheel angle. Pick a target at lookahead distance L and bearing alpha; the formula gives the steering angle whose circular arc passes through it. Short L reacts sharply but wobbles; long L is smooth but cuts corners. The example uses L = 1 m and the speed rule on the right: 0.8 m/s straight, about 0.4 m/s at full lock.

## Slide 29: Exercises
05
Build your controller step by step, then make it fast and consistent

## Slide 30: Your first controller
CONTROLLER.PY · A NAIVE START
import math
from workshop_api import DriveCommand, Observation, wrap_angle
def drive(obs: Observation) -> DriveCommand:
front = obs.sector(-0.2, 0.2)
if not front or min(front) < 0.6: # blocked or unknown
return DriveCommand()
best_angle, best_range = 0.0, 0.0
for i, r in enumerate(obs.ranges): # farthest ray in ±60°
a = wrap_angle(obs.angle_min + i * obs.angle_increment)
if abs(a) < math.radians(60) and r > best_range:
best_angle, best_range = a, r
steering = math.atan2(2 * 0.324 * math.sin(best_angle), 1.0)
return DriveCommand(speed_mps=0.5, steering_rad=steering)
How it works
Stops if the front cone is blocked or unknown
Picks the farthest ray within ±60°
Steers at it with Pure Pursuit (L = 1 m)
Make it better
Slow down when steering hard
Aim at gaps, not single far rays
Add time-to-collision braking
Notes: Here's a deliberately simple controller to get the car moving. It stops if anything is close or unknown ahead, otherwise it steers at the farthest visible point. It will work on gentle tracks and fail in interesting ways on sharp ones; that's the point. Paste it into controller.py, save, and run restart -Controller starter.

## Slide 31: Workshop milestones
1
Connect
Start the simulator and confirm fresh sensor messages in the logs.
2
Stay safe
Keep the car stopped when the forward sector is blocked or unknown.
3
Steer
Implement steering with wall following or Follow the Gap.
4
Slow down
Reduce speed for corners and nearby obstacles.
5
Be consistent
Complete one clean lap, then three more with the same settings.
6
Compare
Compare lap times using the simulator's lap and collision counters.
Notes: These six milestones are the workshop exercises from the README. Work through them in order; each one builds on the last. When comparing changes, write down the controller settings, completed laps and collisions so you can tell whether a change actually helped.

## Slide 32: The edit–test loop and tuning
Every change
Edit and save controller.py
restart -Controller starter
Watch logs -Follow
pause, then reset the car
Knob | Lower | Higher
Lookahead L | Sharper, but twitchy | Smoother, cuts corners
Safety bubble | Squeezes through tight gaps | Safer, may find no gap
Obstacle threshold | Reacts late | Avoids early, fewer gaps
Max speed | Safer, slower laps | Faster, more collisions
Change one knob at a time. Record the settings, laps and collisions for each run.
Notes: This is the rhythm for the rest of the session. No rebuild is ever needed: save, restart, watch the logs, and reset the car when it gets stuck. When tuning, change one thing at a time and keep notes, otherwise you won't know which change helped.

## Slide 33: Troubleshooting
Car stays stopped
The starter returns zero. Implement drive() or select the example; check Connection, Autonomous and the logs.
Changes have no effect
Save the file, then restart -Controller starter. No image rebuild is needed.
Port 4567 is busy
Stop the other project and close its simulator window first.
Download or image pull fails
Check Docker Desktop is running and the network is reachable.
Controller fault
Read the error in the logs, fix it, then restart. A hung controller takes about 3 s to stop.
Notes: The five problems you're most likely to hit. In almost every case the first step is the same: run the logs command and read the last message.

## Slide 34: Where to go after today
Learn
Take the RoboRacer course: perception, planning and control in depth.
roboracer.ai/learn/courses
Build
Follow the open-source build guide and ROS 2 driver stack.
f1tenth.readthedocs.io
Race
Enter the AutoDRIVE Sim Racing League or join a university team.
autodrive-ecosystem.github.io
Keep coding
Try a map-based stack: SLAM, a raceline and Pure Pursuit.
Start from controller.py
Notes: If today hooked you, here's where to go next. The RoboRacer course goes deep on the full autonomy stack. The build documentation shows how to assemble a real car. The AutoDRIVE Sim Racing League lets you compete with no hardware at all. And you can keep working on this workshop's controller at home: the same setup works anywhere Docker runs.

## Slide 35
LIGHTS OUT
Ready, set, race
Sense, plan, act
Your drive() turns one LiDAR snapshot into one command, 20 times a second.
Safety first
Unknown or blocked? Stop. Make it safe before you make it fast.
Measure everything
Change one setting at a time and compare laps and collisions.
Keep handy: README.md · controller.py · workshop_api.py · examples/follow_the_gap.py
Notes: Recap the three ideas, then let people get going. Point them to the README for every command and to the example as a reference once they've tried their own approach.